## Slide 1: Breaking Bulbs Briskly By Bogus Broadcasts
Joe Hall and Ben Ramsey

## Slide 2: Goals
Release some Z-Wave recon tools
Break some fluorescent bulbs

## Slide 3: Z-Wave
Low-rate wireless network protocol
Proprietary: no SDK without NDA!
Big in automation & security systems

## Slide 4: Z-Wave
Notes: With reportedly over 35 million sold since 2005, devices range smart plugs and lightbulbs to door locks and smoke detectors to water valves and smart meters.
(break)
Ben here has been doing security research on a similar wireless protocol called ZigBee for a handful of years.
When I started working for him, he asked me to evaluate the security of Z-Wave.

## Slide 5: What’s Out There?
Open-ZWave
  Open source libraries
  Control devices via Z-Wave USB stick
Z-Force (BH ’13 – Fouladi & Ghanoun)
  Commodity radio
  Custom firmware, closed-source software
Scapy-radio (BH ’14 – Picod et al.)
  Generic wireless sniffer/injector using software-defined radios
  Open source, uses GNU Radio and Scapy

## Slide 6: EZ-Wave
Built on top of Scapy-radio
  Extended support for Z-Wave protocol
Includes 3 tools:
  ezstumbler: network discovery & enumeration
  ezrecon: device interrogation
    Manufacturer / product name
    Software versions
    Supported command classes
    Current state
    Configuration settings
  ezfingerprint
    Determines Z-Wave module generation
    PHY manipulation to exploit differences in transceivers
Not available when encryption is used

## Slide 7: A Note About Security
The protocol supports AES-128
  Up to the device manufacturer to use it…
  Only 9 of 33 devices we tested support encryption
    5 door locks & 4 newer devices
    3 of the 4 were ‘opt-in’ security…

## Slide 8: Demo
Notes: So here’s a quick demo of EZ-Wave.
For time sake, I’m skipping network discovery and go straight to network enumeration.
Up here I have a network setup with a few devices paired.
(demo ezstumbler)
Now, I’m going to use ezrecon to interrogate one of the devices we found.
(demo ezrecon)
(switch to Ramsey)
Well you might ask what the hell this has to do with break bulbs briskly…
(demo of power cycling devices while Ramsey is saying the following)
While EZ-Wave is geared towards reconnaissance, the messages used to interrogate devices are pretty much the same as those used to control them.
We really wanted to break something, so we did some experiments to see how quickly we could break fluorescent bulbs.

## Slide 9: Breaking Bulbs
Z-Wave is not the only smart energy protocol!
2.4 GHz
  Wi-Fi
  ZigBee
  6LoWPAN
  WirelessHART
  Bluetooth
< 1 GHz
  Z-Wave
  Insteon
  Lutron
  Xodus
  …

## Slide 10: Breaking Bulbs
How do you quickly break fluorescent bulbs?
  Turn them on and off rapidly.
C. Spezia and J. Buchanan, “Maximizing the Economic Benefits of Compact Fluorescent Lamps,” J. of Industrial Tech, vol. 27, no. 2, 2011.
At 2 seconds on, 8 seconds off they report:
- Mean CFL failure: 7,300 cycles (20.3 hrs)
- Wide range: 2,000-22,000 cycles (5.6-61.1 hrs)

## Slide 11: Breaking Bulbs
Trust but replicate
  2 seconds on, 8 seconds off
What about industrial lighting?

## Slide 12: Breaking Bulbs
We can break industrial bulbs faster!
1 second on, 3 seconds off is fastest to fail
(Faster cycles do not provide enough thermal stress)

## Slide 13: Breaking Bulbs
Does 1 sec on, 3 secs off also work for residential CFLs?
  Yes!

## Slide 14: Takeaways
Users:
  Be mindful when wireless systems control the real world
  As always… RTFM!
Device Manufacturers:
  Support encryption already…
    We’re tired of waiting!
  Make it the default…
    Let me decide if I don’t want my stuff secure

## Slide 15: Questions
EZ-Wave available @
https://github.com/AFITWiSec/EZ-Wave
Let The Forking Begin!